## Slide 1: Ports

## Slide 2
Port - Interface between the computer and other computers or devices.
Parallel port
Serial port
1 way transmission data from second device
Bi- directional (2 way comm)

## Slide 3: PS/2
Keyboard or mouse port.

## Slide 4: USB (Universal Serial Bus)
can connect computer peripherals such as mouse devices, keyboards, PDAs, gamepads and joysticks, scanners, digital cameras and printers.
The USB icon, found on all USB plugs.
Type-B USB port Type-A USB port
Device components: Any external storage /printer/scanner

## Slide 5: FireWire(Apple) / i.Link(Sony)
serial bus interface standard, offering high-speed communications and isochronous real-time data services.
The FireWire icon, found on all FireWire USB plugs.
The 6-pin and 4-pin FireWire.
Device components: Video camera

## Slide 6
Earphone port
Audio In
LAN / Network port
VGA/Display
SYMBOL’S NAME
DEVICE/COMPONENTS
Earphone/speaker
RJ45/CAT5e cable
Monitor/projector
Earphone/speaker

## Slide 7: Parallel Printer Port
used to connect printers and other add-on items such as external CD-ROM drives, external tape drives, and scanners.
Standard 25-pin D connector / DB-25 connector
Centronic connector and port

## Slide 8: Serial Port (COM port/RS-232 port)
Use for attaching modem, other computers, UPS (uninterruptible power supply) and barcode readers or for configuring Network equipment such as manageable switches and routers.

## Slide 9
Standard 9-pin D-sub connector / DE-9 connector
DB-15
DB-15HD

## Slide 11
24-pin DVI (Digital Visual Interface)

## Slide 12: Expansion Slot
Expansion slot standards
PCI Express
PCI
PCI-X
AGP

## Slide 13: Expansion Slot
Expansion cards type
Graphics cards
Sound cards
Network cards
TV tuner cards
Modems
Host adapters such as SCSI, RAID, SATA controllers, Firewire (universally known as I/O card)
POST cards
Physics cards, only recently became commercially available.
Video processing expansion cards

## Slide 14
PCI (Peripheral Component Interconnect)
Expansion Card Type – all
rear of system front of system
PCI-X (Peripheral Component Interconnect Extended)
Expansion Card Type– Network Card and Host adapter card.
rear of system front of system

## Slide 15
PCI Express (PCIe)
Expansion Card Type – all

## Slide 16
AGP(Accelerated Graphics Port/Advanced Graphic Port)
Expansion Card Type – Graphic Card (3D)

## Slide 17: Storage Interface

## Slide 18: Storage Interface
Floppy Disk Drive (FDD) power cable (Berg connector)
Floppy Disk Drive (FDD) data cable

## Slide 19: Storage Interface (on motherboard)

## Slide 20
PATA ribbon